## Slide 1: Week 06

## Slide 2: Updates
Quiz 2 Review: https://github.com/pattonsgirl/Fall2021-CEG2350/blob/main/Quizzes/Quiz2.md
Lab 04 - 10% off per day until Thursday, 9/30
Lab 05 - Due Tuesday 10/5
Quiz 3 - 10/7
Midterm - 10/14
  1.5 hours once started
  1 attempt
  Open 8:00 AM - 11:59 PM

## Slide 3: Lab 04 Notes
Some good questions that cropped up
  What should be executable?
  What is ~/.profile doing?
  Letting a command have “modes”
    There is a way to properly create “options” instead of string compares
    But I expected use of string compares of arguments passed

## Slide 4: Computer Hardware

## Slide 5: Von Neumann Architecture
Electronic digital computer with features:
Processing unit
  Arithmetic logic until + process registers
Control unit
  Instruction register + program counter
Memory
  Store data + instructions
External mass storage
IO mechanisms
This is still the basis of modern computers

## Slide 6: CPU = Central Processing Unit
Responsible for processing all information from programs run by your computer
Clock speed of CPU governs how fast it executes instructions and is measured in GHz (usually between 1 and 5 GHz)
Usually cooled by a heat sink and fan, or water-cooling system
Most newer CPU includes an on-die graphics processing unit (GPU)
Notes: https://www.computerscience.gcse.guru/theory/von-neumann-architecture
https://en.wikipedia.org/wiki/Computer_hardware
https://www.crucial.com/articles/pc-builders/what-is-computer-hardware

## Slide 7: The CU, ALU, and MU
The CPU contains the ALU, CU and a variety of registers.
The ALU (Arithmetic and Logic Unit) allows arithmetic (add, subtract etc) and logic (AND, OR, NOT etc) operations to be carried out
The CU (Control Unit) controls the operation of the computer’s ALU, memory and input/output devices, telling them how to respond to the program instructions it has just read and interpreted from the memory unit.
The control unit also provides the timing and control signals required by other computer components.
The memory unit consists of RAM, sometimes referred to as primary or main memory
RAM is split into partitions. Each partition consists of an address and its contents (both in binary form)
Notes: https://www.computerscience.gcse.guru/theory/von-neumann-architecture

## Slide 8: CPU Registers
Registers are high speed storage areas in the CPU. All data must be stored in a register before it can be processed
Notes: https://www.computerscience.gcse.guru/theory/von-neumann-architecture

## Slide 9: CPU - Fetch execute cycle
Basic instruction cycle of the CPU
  AKA. Fetch, decode, execute cycle
Notes: https://www.computerscience.gcse.guru/theory/fetch-execute-cycle

## Slide 10: RAM
RAM = Random Access Memory
Stores the code and data that are being actively accessed by the CPU
Volatile – contents are erased if power is lost
MOS memory chips store data on memory cells consisting of MOSFETs and MOS capacitors
Notes: https://www.redhat.com/sysadmin/memory-and-storage
https://www.crucial.com/articles/about-memory/support-what-does-computer-memory-do

## Slide 11: HDD
HDD = Hard Disk Drive
Non-volatile – information persists after power reset
Data is stored on platters
Data stored magnetically
Disk fragmentation over time
Notes: https://blogs.umass.edu/Techbytes/2017/04/04/hard-drives-how-do-they-work/
https://cs.stanford.edu/people/nick/how-hard-drive-works/
https://en.wikipedia.org/wiki/Computer_hardware

## Slide 12: Fragmentation

## Slide 13: How do reads & writes happen?
Temporarily stored on HDD cache while head wanders around to correct areas
Head magnetizes the data to the disk
  Never forget - at some point it’s all binary!
Notes: https://en.wikipedia.org/wiki/Computer_data_storage

## Slide 14: SSD
SSD = Solid State Drive
Stores data on semi-conductor cells
  Data in bits are stored on these cells
Has a built in controller
  Wear leveling
  Read & write caching
Non-volatile
Notes: https://en.wikipedia.org/wiki/Solid-state_drive

## Slide 15: HDD vs SSD: Pros and Cons
SSD’s are faster in terms of data access & read / write speeds
HDD failures are easier to detect
  Slow down of head movements over time
  Loud noises since it’s all mechanical
SSDs don’t do scary noises – can use software to detect decrease in read / write speeds that would point to failure

## Slide 16: “Virtual” Memory
Memory on CPU cache & RAM – chip based, finite.
Memory on disk – finite, but large. Can define some space as overload
Use cases:
  Putting a PC in “sleep” mode
  Keep active areas / processes in RAM, offload rest
Notes: https://www.howtogeek.com/126430/htg-explains-what-is-the-windows-page-file-and-should-you-disable-it/
https://www.thegeekdiary.com/beginners-guide-to-swap-space-management-in-linux/
https://www.internalpointers.com/post/introduction-virtual-memory

## Slide 17: How does virtual memory work?
CPUs now have an MMU
  Memory Management Unit
The MMU has a map of addresses
  Think 0 - x addresses on RAM 0 - x addresses on disk
  CPU only cares that it get the info. The MMU acts as translator
This also allows virtual memory to be contiguous
  Processes / programs also like thinking they have a reserved “block” of memory, even if it is actually split between RAM and disk
This is tracked on a page table, stored in the MMU
Notes: https://www.internalpointers.com/post/introduction-virtual-memory
http://csapp.cs.cmu.edu/2e/ch9-preview.pdf

## Slide 18: Motherboard
Buses to facilitate communication of devices
RAM & CPU have dedicated bus between them
RAM has busses to other spots (HDD, GPU, etc)
Has specific hardware it can support
  CPU sockets that handle specific CPU pins, for example
$ lshw
  All hardware connected to system
msinfo
Notes: https://computer.howstuffworks.com/motherboard3.htm

## Slide 19: Motherboard
Houses the CPU and is a hub that all other hardware runs through
Acts as a brain; allocating power where it’s needed, communicating with and coordinating across all other components
The chipset is part of the motherboard's logic system and is usually made of two parts -- the northbridge and the southbridge.
  These two "bridges" connect the CPU to other parts of the computer.
  Each bridge is a separate chipset on the motherboard
BIOS / UEFI is on ROM chip on motherboard
https://www.tomshardware.com/reviews/motherboard-parts-explained,5669.html
Notes: https://www.crucial.com/articles/pc-builders/what-is-computer-hardware
https://pediaa.com/difference-between-northbridge-and-southbridge/

## Slide 20: ROM
ROM = Read only memory
Non-volatile chip
Stores the BIOS that runs when the computer is powered on or otherwise begins execution
These days ROM and the BIOS is a fuzzy line
  You can update it

## Slide 21: GPU = Graphical Processing Unit
Specialized electronic circuit designed to rapidly manipulate and alter memory to accelerate the creation of images in a frame buffer intended for output to a display device
Dedicated:
  A separate card that has its own power lines, ram (VRAM) and cache
Integrated:
  CPU & GPU capabilities combined. CPU gets priority
Discussion on needs (when to choose)
Notes: https://www.makeuseof.com/tag/can-shared-graphics-finally-compete-with-a-dedicated-graphics-card/
https://www.reddit.com/r/explainlikeimfive/comments/pdxy6s/eli5_why_does_a_computer_need_a_dedicated/
https://en.wikipedia.org/wiki/Graphics_processing_unit

## Slide 22: Class Builds a PC
Can play Destiny 2
Can dual boot?
Can experiment with machine learning

## Slide 23: Lab 05 Notes
$ whoami
$ whois
$ echo $EUID
Little ID checker script
For system discovery parts:
  Part 1: write details for your system
  Part 2: use commands to find system information
    The commands are mostly provided. What the command is showing you is not ;) Check out those man pages and google searches

## Slide 24
#! /bin/bash
echo $EUID
if [[ $EUID -eq 1000 ]]
then
echo "Hello ubuntu"
fi

## Slide 25: The Boot Process
In this part, we will assume a PC with an OS installed

## Slide 26: BIOS / UEFI
BIOS = Basic Input Output System
UEFI = Unified Extensible Firmware Interface
Stored on chip on motherboard
Detects boot partitions on connected devices (disks or external drives)
UEFI is the correct modern word. Most people still refer to it as the BIOS, and UEFI is assumed

## Slide 27: POST
Power On Self Test
Checks hardware for compatibility & connectivity
Where the beep codes come from – which piece of hardware failed to pass muster
Once POST is done, hand back to BIOS

## Slide 29
Notes: https://www.howtogeek.com/56958/htg-explains-how-uefi-will-replace-the-bios/
https://www.partitionwizard.com/partitionmagic/uefi-vs-bios.html

## Slide 30: MBR & GPT
Primary partition tables
  Hold the system bootloader
  MBR = Master Boot Record (use with BIOS / legacy mode)
  GPT = GUID Partition Table
Partition tables determine:
  Which partition(s) are bootable
  Where partitions start / end
Notes: https://www.howtogeek.com/193669/whats-the-difference-between-gpt-and-mbr-when-partitioning-a-drive/
https://www.diskgenius.com/how-to/mbr-vs-gpt.php

## Slide 31: MBR
MBR = Master Boot Record
MBR holds the partition table and boot loader in the same partition
  This is not great for recovery if the info is corrupted
There are 4 primary partitions at most on MBR disk. The 64 bytes in the first sector is used to save partition information, and each partition requires 16 bytes.
Works with disk capacity up to 2 TB
BIOS uses disks with MBR partition schemes
A UEFI BIOS would need to have “legacy” mode enabled to read disks with MBR
Notes: https://www.diskgenius.com/how-to/mbr-vs-gpt.php

## Slide 32: GPT
Bootloader is stored in EFI partition
  Peek at this in Windows using the Disk Partition Manager
Reserve MBR. On GPT disk, the first physical sector on is still MBR which has talked in previous part. This MBR here does not have actual function and it exists only due to the consideration of software compatibility.
Primary GPT header stores right behind protective MBR on second physical sector. The GPT header defines partition number. Basically, you can deem that there is no limitation on partition number of GPT disk.
In fact, the third sector is the beginning of the actual partition table. Please note that each sector can store 4 partitions' information, which means every partition needs 128 bytes to store partition information.
Notes: https://www.diskgenius.com/how-to/mbr-vs-gpt.php

## Slide 33: MBR vs. GPT
If your BIOS is in UEFI mode, disks cannot use MBR only GPT
GPT supports up to 9.4 ZB disk capacity
  vs MBR at 2TB cap
GPT supports up to 128 partitions
  vs 4 primary partition cap on MBR
Notes: https://www.diskgenius.com/how-to/mbr-vs-gpt.php
https://neosmart.net/wiki/mbr-boot-process/

## Slide 34: Bootloader ToDos
Notes: https://neosmart.net/wiki/mbr-boot-process/
https://medium.com/@workrockin/what-are-bootloaders-54933fec4bb5

## Slide 35: Bootloaders

## Slide 36: Most common bootloaders

## Slide 37: Boot Menu Options Include
Choose OS or version of OS
Safety mode
Memory diagnostic tool
Bootloader passes control to kernel
Kicks off initial processes to load OS

## Slide 38: Grub
Notes: https://linuxhint.com/what-is-a-boot-loader/

## Slide 39: Why people love grub…
https://www.addictivetips.com/ubuntu-linux-tips/best-grub2-bootloader-themes-on-linux/

## Slide 40: BootMGR
Notes: https://linuxhint.com/what-is-a-boot-loader/

## Slide 41: Kernels
Interface between hardware and OS
Memory management:
  Keep track of how much memory is used to store what, and where
Process management:
  Determine which processes can use the central processing unit (CPU), when, and for how long
Device drivers:
  Act as mediator/interpreter between the hardware and processes
System calls and security:
  Receive requests for service from the processes
Notes: https://www.redhat.com/en/topics/linux/what-is-the-linux-kernel

## Slide 42: Linux Kernel
The kernel is the version number - the core of the system
OS is the “Pretty Name” that determines how the user space runs
  https://distrowatch.com/

## Slide 43
The Kernels
The GRUB Menu

## Slide 44: Windows Kernel
Winload.exe (Windows Boot Loader) is a small piece of software, called a system loader, that's started by BOOTMGR, the boot manager used in Windows 10, Windows 8, Windows 7, and Windows Vista operating systems.
The job of winload.exe is to load essential device drivers, as well as ntoskrnl.exe, a core part of Windows.
Notes: https://www.lifewire.com/what-is-winload-exe-2626051